Instructors Introduction to Shrimping.it
Jeremy Bennett & Simon Cook, Embecosm

---
Persistence of Vision

---
Arduino and Shrimping.it
- Arduino
  - low cost (~£20) 8-bit microcontroller for hobbyists
  - based on Atmel ATMega328 chip
  - 1 million sold worldwide
- Shrimping.it
  - breadboard version of Arduino
  - gives students hands-on experience
  - much cheaper (£4 parts, £2 programming cable)

---
Preparation
- Ensure your pupils can each access a USB port
- Ensure the Arduino IDE is installed
  - http://arduino.cc/en/main/software
- Ensure the FTDI Windows/Mac drivers are installed
  - http://www.ftdichip.com/FTDrivers.htm
  - not needed with an recent Linux
- Download and unzip the PoV software
  - http://tinyurl.com/shrimpovcode
  - or ensure your pupils have access to do this
- Try it out for yourself first!

---
Breadboard

---
The Minimal Shrimp

---
Minimal Shrimp Circuit

---
A Blinking Light
22pF capacitors
labeled “22J”
LED long leg on the left
100nF capacitor
labeled “104”
100Ω resistor
brown-black-brown
gold on the end
10kΩ resistor
brown-black-orange
gold on the end

---
Loading the Blink Program
Note on Linux, you may have to be in the dialout and/or lock groups.

---
Blink Circuit Diagram

---
Ardunio/Shrimp Programming
- Programmed in C/C++
- Supplemented by the Wiring library
  - makes common hardware operations easy
- Only need to define two functions
  - setup called once on reset
  - loop called repeatedly thereafter
- A good opportunity to learn a major language
  - requires syntactic discipline
  - but scales for BIG projects

---
Persistence of Vision
22pF capacitors
labeled “22J”
LED long leg on the left
100nF capacitor
labeled “104”
10kΩ resistor
brown-black-orange
gold on the end

---
Loading the POV Program
http://tinyurl.com/shrimpovcode

---
Shrimp Persistence of Vision

---
Shrimp PoV with a Battery

---
Shrimp PoV Circuit

---
ATMega328 Pinout

---
The Protected Shrimp