Persistence of Vision with Shrimping.it
Jeremy Bennett & Simon Cook, Embecosm

---
Arduino and Shrimping.it
- Arduino
  - low cost (~£20) 8-bit microcontroller for hobbyists
  - based on Atmel ATMega328 chip
  - 1 million sold worldwide
- Shrimping.it
  - breadboard version of Arduino
  - gives students hands-on experience
  - much cheaper (£4 parts, £2 programming cable)

---
Breadboard

---
A Blinking Light
22pF capacitors
labeled “22J”
LED (shines red) long leg on the left
100nF capacitor
labeled “104”
100Ω resistor
brown-black-brown
gold on the end
Notch in the end of the chip
Dot by pin 1 of the chip
10kΩ resistor
brown-black-orange
gold on the end

---
Loading the Blink Program
Note on Linux, you may have to be in the dialout and/or lock groups.

---
Persistence of Vision
22pF capacitors
labeled “22J”
LED (shines red) long leg on the left
100nF capacitor
labeled “104”
Notch in the end of the chip
Dot by pin 1 of the chip
10kΩ resistor
brown-black-orange
gold on the end

---
Loading the POV Program
http://tinyurl.com/shrimpovcode

---
Shrimp PoV with a Battery

---
Shrimp PoV Circuit

---
ATMega328 Pinout

---
Ardunio/Shrimp Programming
- Programmed in C/C++
- Supplemented by the Wiring library
  - makes common hardware operations easy
- Only need to define two functions
  - setup called once on reset
  - loop called repeatedly thereafter
- A good opportunity to learn a major language
  - requires syntactic discipline
  - but scales for BIG projects

---
The Protected Shrimp