www.embecosm.com
EWH3: Shrimping Persistence of Vision Kit
Notes for Users
About
Persistence of vision is when a brief bright image (such as from an LED) stays fixed on your retina. By flashing a row of LEDs very fast and then waving them in front of someone, we can use this to spell out a message.
Tool set up
Install the Arduino IDE from arduino.cc/en/main/software. If running on Windows, install the Silicon Labs CP210x USB to UART Bridge drivers from www.silabs.com/products/mcu/Pages/USBtoUARTBridgeVCPDrivers.aspx.
When using the Arduino IDE, set up for Arduino Uno.
Circuit layout

22pF capacitors labeled “22J”
LED (shines red) long leg at the bottom
100nF capacitors labeled “104”
Notch in the end of the chip
Dot by pin 1
22pF capacitors labeled “22J”
10kΩ resistor
brown-black-orange
gold on the end

Note. Capacitor color may vary in different kits
Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com

The programs
Download the persistence of vision code from tinyurl.com/shrimpovcode. Unzip it and either open it from the Arduino IDE, or copy it to the IDE's sketchbook folder (find from the IDE preferences menu), so it appears in the list of example programs when you start up the IDE.
Kit contents
The kit contains parts to build the persistence of vision circuit in the minimal form shown here, with a 75Ω resistor used in the “blink” circuit.
1 x battery box	2 x 22pF capacitor
3 x AA battery	1 x 10kΩ resistor
270 hole breadboard (BB-301 type)	1 x 16MHz quartz crystal
7 x assorted wires	1 x 75Ω resistor
1 x Atmel ATMega328-PU	8 x 100mCd red LED
1 x 100nF capacitor	1 x rubber band
Embecosm EHW5 USB-UART Bridge

More information
A detailed tutorial is in preparation. The draft of this, along with all design and tutorial material is on GitHub (github.com/embecosm/shrimp-pov). It is all based on Cefn Hoile's original work at shrimping.it.
For more information about Embecosm, including careers in open source compiler development, please visit www.embecosm.com.

Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com
EWH3: Shrimping Persistence of Vision Kit
Notes for Users
About
Persistence of vision is when a brief bright image (such as from an LED) stays fixed on your retina. By flashing a row of LEDs very fast and then waving them in front of someone, we can use this to spell out a message.
Tool set up
Install the Arduino IDE from arduino.cc/en/main/software. If running on Windows, install the Silicon Labs CP210x USB to UART Bridge drivers from www.silabs.com/products/mcu/Pages/USBtoUARTBridgeVCPDrivers.aspx.
When using the Arduino IDE, set up for Arduino Uno.
Circuit layout

22pF capacitors labeled “22J”
LED (shines red) long leg at the bottom
100nF capacitors labeled “104”
Notch in the end of the chip
Dot by pin 1
22pF capacitors labeled “22J”
10kΩ resistor
brown-black-orange
gold on the end

Note. Capacitor color may vary in different kits
Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com

The programs
Download the persistence of vision code from tinyurl.com/shrimpovcode. Unzip it and either open it from the Arduino IDE, or copy it to the IDE's sketchbook folder (find from the IDE preferences menu), so it appears in the list of example programs when you start up the IDE.
Kit contents
The kit contains parts to build the persistence of vision circuit in the minimal form shown here, with a 75Ω resistor used in the “blink” circuit.
1 x battery box	2 x 22pF capacitor
3 x AA battery	1 x 10kΩ resistor
270 hole breadboard (BB-301 type)	1 x 16MHz quartz crystal
7 x assorted wires	1 x 75Ω resistor
1 x Atmel ATMega328-PU	8 x 100mCd red LED
1 x 100nF capacitor	1 x rubber band
Embecosm EHW5 USB-UART Bridge

More information
A detailed tutorial is in preparation. The draft of this, along with all design and tutorial material is on GitHub (github.com/embecosm/shrimp-pov). It is all based on Cefn Hoile's original work at shrimping.it.
For more information about Embecosm, including careers in open source compiler development, please visit www.embecosm.com.

Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com
EWH3: Shrimping Persistence of Vision Kit
Notes for Users
About
Persistence of vision is when a brief bright image (such as from an LED) stays fixed on your retina. By flashing a row of LEDs very fast and then waving them in front of someone, we can use this to spell out a message.
Tool set up
Install the Arduino IDE from arduino.cc/en/main/software. If running on Windows, install the Silicon Labs CP210x USB to UART Bridge drivers from www.silabs.com/products/mcu/Pages/USBtoUARTBridgeVCPDrivers.aspx.
When using the Arduino IDE, set up for Arduino Uno.
Circuit layout

22pF capacitors labeled “22J”
LED (shines red) long leg at the bottom
100nF capacitors labeled “104”
Notch in the end of the chip
Dot by pin 1
22pF capacitors labeled “22J”
10kΩ resistor
brown-black-orange
gold on the end

Note. Capacitor color may vary in different kits
Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com

The programs
Download the persistence of vision code from tinyurl.com/shrimpovcode. Unzip it and either open it from the Arduino IDE, or copy it to the IDE's sketchbook folder (find from the IDE preferences menu), so it appears in the list of example programs when you start up the IDE.
Kit contents
The kit contains parts to build the persistence of vision circuit in the minimal form shown here, with a 75Ω resistor used in the “blink” circuit.
1 x battery box	2 x 22pF capacitor
3 x AA battery	1 x 10kΩ resistor
270 hole breadboard (BB-301 type)	1 x 16MHz quartz crystal
7 x assorted wires	1 x 75Ω resistor
1 x Atmel ATMega328-PU	8 x 100mCd red LED
1 x 100nF capacitor	1 x rubber band
Embecosm EHW5 USB-UART Bridge

More information
A detailed tutorial is in preparation. The draft of this, along with all design and tutorial material is on GitHub (github.com/embecosm/shrimp-pov). It is all based on Cefn Hoile's original work at shrimping.it.
For more information about Embecosm, including careers in open source compiler development, please visit www.embecosm.com.

Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com
EWH3: Shrimping Persistence of Vision Kit
Notes for Users
About
Persistence of vision is when a brief bright image (such as from an LED) stays fixed on your retina. By flashing a row of LEDs very fast and then waving them in front of someone, we can use this to spell out a message.
Tool set up
Install the Arduino IDE from arduino.cc/en/main/software. If running on Windows, install the Silicon Labs CP210x USB to UART Bridge drivers from www.silabs.com/products/mcu/Pages/USBtoUARTBridgeVCPDrivers.aspx.
When using the Arduino IDE, set up for Arduino Uno.
Circuit layout

22pF capacitors labeled “22J”
LED (shines red) long leg at the bottom
100nF capacitors labeled “104”
Notch in the end of the chip
Dot by pin 1
22pF capacitors labeled “22J”
10kΩ resistor
brown-black-orange
gold on the end

Note. Capacitor color may vary in different kits
Freely available under a Creative Commons Attribution-ShareAlike license
www.embecosm.com

The programs
Download the persistence of vision code from tinyurl.com/shrimpovcode. Unzip it and either open it from the Arduino IDE, or copy it to the IDE's sketchbook folder (find from the IDE preferences menu), so it appears in the list of example programs when you start up the IDE.
Kit contents
The kit contains parts to build the persistence of vision circuit in the minimal form shown here, with a 75Ω resistor used in the “blink” circuit.
1 x battery box	2 x 22pF capacitor
3 x AA battery	1 x 10kΩ resistor
270 hole breadboard (BB-301 type)	1 x 16MHz quartz crystal
7 x assorted wires	1 x 75Ω resistor
1 x Atmel ATMega328-PU	8 x 100mCd red LED
1 x 100nF capacitor	1 x rubber band
Embecosm EHW5 USB-UART Bridge

More information
A detailed tutorial is in preparation. The draft of this, along with all design and tutorial material is on GitHub (github.com/embecosm/shrimp-pov). It is all based on Cefn Hoile's original work at shrimping.it.
For more information about Embecosm, including careers in open source compiler development, please visit www.embecosm.com.

Freely available under a Creative Commons Attribution-ShareAlike license